## Slide 1: RNN-Based Voice Stability Monitor
PS-01 · SUDARSHANA SEMICONDUCTORS VLSI HACKATHON
A low-power GRU accelerator, taken from RTL to GDSII on a 0.18 µm library with Cadence Genus, Innovus and Tempus.
Team 18
Magesh · 24BVD1048 R Naga Arjun · 24BVD1102
powerhouse
Notes: Introduce the team and the problem statement PS-01. Fill in the date.

## Slide 2: Detecting a bad call on the device, not in the cloud
Telecom edge devices must spot degraded call quality in real time, without sending audio away.
Live call
16 features per frame arrive as INT8.
Edge device
A small GRU scores each frame on chip.
Alert
A smoothed score raises an interrupt.
Under 1 ms per frame
INT8 weights
INT16 activations
Low-milliwatt power
Team 18 · powerhouse

## Slide 3: Architecture
Sequencer FSM
Weight memory: 1552 bytes + 49 INT16 biases
Register file
AXI-Stream in
16 × INT8, tlast on beat 16
Frame buffer
Shared MAC
16×8 MAC + 17×18 gating multiplier
Sigmoid and tanh LUTs
256 entries
Gate update
Hidden state
16 × INT16, flush
Output layer
score
Shift-based EMA
Alert with hysteresis
Interrupt
Arrows show the data flow: left to right on the top row, wrapping from Gate update to Hidden state on the second row. The sequencer drives one time-shared datapath.
Team 18 · powerhouse

## Slide 4: Trading speed we do not need for area
Fully parallel GRU
Many multipliers working at once. Fast, but large and power hungry.
Our time-multiplexed GRU
One multiplier path reused for every term. About 1573 cycles per frame.
15.73 µs
at 100 MHz
23.6 µs
at the 15 ns signoff clock
1 ms
budget per frame
Area and power are the primary metrics, so the design spends cycles we have to spare.
Team 18 · powerhouse

## Slide 5: Number formats and accuracy
Quantity | Format
Features | INT8
Weights | INT8, Q.6
Biases | INT16, Q.14
Activations | INT16, Q1.14
Accumulator | INT32
LUTs | 256 entries
0.0043
score rms error vs float
0.026
score max error vs float
0.0078
sigmoid LUT max error
0.031
tanh LUT max error
0 of 2000 alert decisions differ from the float model.
Team 18 · powerhouse

## Slide 6: RTL-to-GDSII flow
Golden model + QAT
Python
RTL
Verilog
Regression
ncsim
Synthesis
Genus 21.1
Place and route
Innovus 21.15
Signoff
Tempus 22.11
GLS + SAIF
ncsim
GDSII
Innovus
Genus synthesis result: 30,970 leaf cells across 2 modules.
Team 18 · powerhouse

## Slide 7: Verification: bit-exact against the model
3 seeds × 2000 frames in ncsim, 0 errors.
200 gate-level frames, 0 errors.
Reset and flush mid-compute
Early tlast
Saturated inputs
Back-to-back frames
Threshold crossed both ways: 5 assertions, 5 deassertions
One-hour stream (360,000 frames) passes in the model with 442 alert assertions. Correlation 0.956 against a synthetic quality label.
Team 18 · powerhouse

## Slide 8: Implementation results
1.255 mm²
cell area
30,970
cells
66.7 MHz
15 ns, positive slack
23.6 µs
latency per frame
Check | Result
Post-route setup WNS | +0.165 ns
Post-route hold WNS | +0.122 ns
Tempus setup | +0.237 ns
Tempus hold | +0.840 ns
DRC | 0
Connectivity | clean
Antenna | 1 violation
Team 18 · powerhouse
Clock tree debugger, dc_slow: 14,398 sinks
Final routed layout

## Slide 9: Power: above target, and we say so
Vectorless (Genus): 80.8 mW
Activity-based (Tempus, SAIF): 23.88 mW
The brief asks for low-milliwatt power. Both numbers sit above that goal. Bar lengths are to scale.
Sequential cells draw 73.9% of power.
The weight array is about 92% of the flops.
Fixes: clock gating, a 10 MHz clock, and duty cycling.
One frame keeps the core busy about 0.16% of a 10 ms period at 100 MHz, 1.6% at 10 MHz.
Team 18 · powerhouse

## Slide 10: Limitations and next steps
Team 18 · powerhouse
Where we fall short
The GDS has no foundry map or standard-cell merge, because the 0.18 µm GDS was not available.
Power is above target.
497 nets exceed the max-fanout limit.
Fault injection and coverage were not run.
Next steps
Pipeline the multiplier if 100 MHz is required.
Try the RAM macros in the LEF for the weights.
Add clock gating.
Backup: antenna markers, 1 violation in the final run versus 150 in the first.

## Slide 11
Thank you
scripts/run_rtl_ncsim.sh
Run the demo with one command. It prints the frames passing, with the alert asserting and clearing.
https://github.com/RKNAGA18/vsm-gru-asic
Source code and scripts
Notes: Run the script live. Point out the pass count and the alert assert and clear lines.